## Slide 1: Fingerprint-Based Machine Learning Prediction of Chemical Properties
Department of Chemical Engineering,
King monkut’s Institute of Technology Ladkrabang
Sukit | Kerdsawat | 63010987
Ekkaparb | Parisupat | 63011091
Presented by
Advisor
Assoc. Prof. Dr. Amata Anantpinijwatna

## Slide 2: Table of contents
Introduction
2
3
4
Methodology
Result
Conclusion
1

## Slide 3
First Semester

## Slide 4
Fig 1. Chemical Experiment
Background, Object and Scope
Introduction
Ref [1] : Thermodynamics in process development in the chemical industry, https://doi.org/10.1016/0378-3812(91)85029-T
    Selection of suitable substances for production processes is a long-standing problem in the petrochemical industry. Development of a model by using machine learning (ML) become more popular because they are faster and more accurate than the traditional methods
To study the converting of SMILE structures into molecular fingerprints.
To model and improve the accurate of prediction model on Tb and Psat of substances from molecular fingerprints using machine learning and techniques.
To study Tb and Psat of pure organic compound that contain C, H, O and N atom and Number of C atom is 1-12 atom
To study morgan fingerprint that one of tool in RDKit Library using Python Programming Language
Objective
Scope
Notes: Intro
In the industry, there is continuous development and improvement of manufacturing processes. Therefore, selecting substances with properties suitable for these process is critically important and a long-standing issue.
The development of predictive modeling for substance properties using ML (Machine Learning) has become increasingly popular due to its speed and more accurate predictions compared to traditional methods, such as Group Contribution.
Objective
Our project aims to study the development of predictive models for properties with the following objectives:
To study the transformation of from molecular structure formulas, SMILES to Molecular Fingerprint,
To create and enhance the accuracy of predictive models for boiling point (Tb) and vapor pressure (Psat) using ML and related ML techniques.
Scope
The scope of study includes:
To study the boiling point (Tb) and Vapor pressure (Psat) of pure organic substances composed of CHON and containing 1-12 carbon atoms.
To study the application of Morgan Fingerprint with ML.
ในอุตสาหกรรมนั้นมีการพัฒนาปรับปรุงกระบวนการผลิตอยู่ตลอดเวลา การคัดเลือกสารที่มีสมบัติที่เหมาะสมกับกระบวนการผลิตนั้นจึงเป็นเรื่องที่สำคัญอย่างยิ่งและเป็นปัญหาที่มีอย่างยาวนาน
การพัฒนาแบบจำลองทำนายสมบัติสารโดยใช้ ML เป็นที่นิยมมากยิ่งขึ้นเนื่องจากมีความรวดเร็วและผลทำนายแม่นยำกว่าวิธีการแบบดั้งเดิม เช่น Group Contribution
Project ของเราจึงได้ทำการศึกษาวิธีการพัฒนาแบบจำลองทำนายสมบัติ โดยมีวัตถุประสงค์และขอบเขตการศึกษาดังต่อไปนี้
เพื่อศึกษาการแปลงสูตรโครงสร้างโมเลกุล SMILES ให้กลายเป็น Molecular Fingerprint,
เพื่อสร้างและเพิ่มความแม่นยำของแบบจำลองทำนาย Tb และ Psat โดยใช้ ML และเทคนิคเกี่ยวกับ ML ที่เกี่ยวข้อง
สำหรับขอบเขตที่ศึกษได้นั้น ได้แก่
เพื่อศึกษา Tb, Psat ของสารอินทรีย์บริสุทธิ์ที่มีองค์ประกอบเป็น CHON และมี C ตั้งแต่ 1-12 atom
และขอบเขตข้อสุดท้ายของงานนี้คือ ศึกษาการประยุกต์ใช้ Morgan Fingerprint กับ ML

## Slide 5
Introduction
Error Metric | Previous Work [2] | This Work
MAE | 5.86 | 3.20
MAPE(%) | 1.47 | 0.84
RMSE | 7.92 | 4.70
R2 | 0.98 | 0.99
Ref [2] : Novel method for properties prediction of pure organic compounds using machine learning, https://doi.org/10.1016/B978-0-323-88506-5.50068-1.
Review Previous Work
Table 1. Performance of Each Work on Tb Prediction Model within CH Scope
Fig 2. Comparison Tb Work on CH Scope
Notes: Our group has studied the fingerprints (FP) and applied them to the dataset from senior projects.
We found that it can also be used to create predictive models for the boiling point (Tb) within the CH scope, and it has better performed , as illustrated by graphs and tables showing the model's performance.
กลุ่มของเราได้ศึกษา FP แล้วนำมาประยุกต์ใช้กับชุดข้อมูลของงานรุ่นพี่ พบว่าสามารถใช้สร้างแบบจำลองทำนาย Tb สำหรับขอบเขต CH ได้เหมือนกัน แล้วก็มีประสิทธิภาพมากกว่า ดังกราฟและตารางแสดงประสิทธิภาพของโมเดล

## Slide 6
Review Previous Work
Introduction
The Previous work (Nattasinee and colleagues) [2] use Machine Learning (ML) by convert the representation of molecule from text format (SMILES) into numbers in the following table while This work convert SMILES to “Molecular Fingerprint”
Ref [2] : Novel method for properties prediction of pure organic compounds using machine learning, https://doi.org/10.1016/B978-0-323-88506-5.50068-1.
SMILES | C | Double | Triple | Branch | Cyclic | Actual Tb | Predict Tb Previous Work [2] | Predict Tb This Work
C1CCC=CCC1 | 7 | 1 | 0 | 0 | 1 | 388.15 | 375.85 | 387.34
CC1=CCCCC1 | 7 | 1 | 0 | 0 | 1 | 383.45 | 375.85 | 377.95
CC1CCC=CC1 | 7 | 1 | 0 | 0 | 1 | 375.85 | 375.85 | 370.31
  Same
  Features
Table 2. Compare Prediction Between Each Work of Similar Structure Substance
  Similar
  SMILES
  Same
  Predictions
Notes: Besides accuracy, it also solved a problem identified in senior projects, related to "substances with similar structures but identical predictive features/ independent variables "
Therefore, Our work utilized Morgan Fingerprint, allowing for distinct predictive variables
Ultimately, this allowed us to distinguish similar substances better and enhanced the accuracy of the model predicting boiling point (Tb)
นอกจากเรื่องความแม่นยำแล้ว ยังแก้ปัญหาที่เจอของงานรุ่นพี่ได้อีกด้วย เป็นปัญหาที่ “สารที่มีโครงสร้างคล้ายกัน แต่มี Feature/ตัวแปรต้นที่ใช้ทำนาย เหมือนกัน”
งานของเราจึงได้นำ Morgan Fingerprint มาใช้ ทำให้สามารถได้ “ตัวแปรต้น” ที่ต่างกัน
ผลสุดท้าย ทำให้แยกสารที่คล้ายกันได้ และยังทำให้แบบจำลองทำนาย Tb มีความแม่นยำมากยิ่งขึ้น

## Slide 7
Result
Introduction
Dataset | MAE | MAPE (%) | RMSE | R2
Train | 20.42 | 4.51 | 30.38 | 0.83
Test | 26.72 | 5.94 | 43.40 | 0.66
Table 3. Performance on Tb Prediction Model within CHON Scope
Fig 3. Best Tb model on CHON Scope
Notes: Our first term project expanded its scope from CH to CHON. According to the model performance results, the model achieves an acceptable level of prediction accuracy, as evidenced by a small error margin between the training and testing datasets, a Mean Absolute Percentage Error (MAPE) of less than 10%, and an R² value greater than 0.5.
ทำให้งานเทอมแรกของกลุ่มเรา ขยายขอบเขตจากเดิม CH เป็น CHON จากตารางแสดงผลลัพธ์ประสิทธิภาพของแบบจำลอง แสดงให้ว่า แบบจำลองนี้สามารถทำนายได้อยู่ในระดับพอรับได้ ซึ่งสามารถสังเกตุได้จาก ค่า Error ระหว่างชุดข้อมูล Train และ Test ไม่ได้ห่างกันมาก, MAPE < 10% และมีค่า R2 >0.5

## Slide 8
Introduction
The functional group that this Tb prediction model can predict well is that the group that have condition with R2 ≥0.5 and MAPE ≤10%
Acceptable: Ester, Alkene, Ketone, Alkane, Amine, Alcohol, Alkyne
Unacceptable: Amide, Aldehyde, Aromatic, Carboxylic Acid, Ether
Fig 4. Tb Prediction on CHON Scope Group by Functional Group
Result
Notes: From the results of the model in the first term, this term we were able to categorize the prediction results by functional group, as follows:
Functional groups where the model achieves acceptable results, indicated by an R² value greater than 0.5 and a Mean Absolute Percentage Error (MAPE) of less than 10%,
  are highlighted with a green frame in the figure.
  Meanwhile, functional groups that do not meet these criteria are highlighted with a red frame in the figure.
จากผลแบบจำลองในเทอมแรก เทอมนี้เราได้แยกผลการทำนายของแบบจำลองนี้แยกออกเป็นตามหมู่ฟังก์ชั่นได้ผลลัพธ์มาดังต่อไปนี้ หมู่ฟังก์ชั่นที่แบบจำลองนี้สามารถทำนายแล้วผลยอมรับได้ จะเป็นหมู่ฟังก์ชั่นที่มีค่าความแม่นยำ R2>0.5,MAPE < 10% ด้วยกรอบสีเขียวดังรูป
ในขณะที่หมู่ฟังก์ชั่นที่ไม่ผ่านเงื่อนไข แสดงด้วยกรอบสีแดงดังรูป

## Slide 9
Second Semester

## Slide 10
Data Collection
Database Source | Datapoint
Hall, K. R. Vapor Pressure and Antoine Constants for Hydrocarbons, and S, Se, Te, and Halogen Containing Organic Compounds. Springer, 1999. | 6,346
Dykyj, J., and K. R. Hall. “Vapor Pressure and Antoine Constants for Oxygen Containing Organic Compounds”. 2000. | 
Hall, K. R. Vapor Pressure and Antoine Constants for Nitrogen Containing Organic Compounds. Springer, 2001. | 
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Ref [3] : Vapor Pressure (chemicals.vapor_pressure) , https://chemicals.readthedocs.io/chemicals.vapor_pressure.html?highlight=vapor%20pressure#rc9de082557a5-4
The Total amount of Substance that be included in CHON is 2,246 datapoints.
Methodology
Table 4. ChEDL Database Collection
Notes: Next, for this term's work, we focus on developing a model to predict Psat, a property that depends not only on the substance species but also on its temperature.
The process begins with data collection from the sources listed in the table. However, only 2246 substances fall within our study's scope.
ถัดมาจะเป็นงานของเทอมนี้นะครับ คือ การพัฒนาแบบจำลองทำนาย Psat ซึ่งเป็นสมบัติที่ไม่ได้ขึ้นอยู่กับแค่ชนิดสารแล้วนะครับ แต่ยังขึ้นกับอุณหภูมิของสารดังกล่าวด้วย
โดยเริ่มต้นจาก การเก็บข้อมูลนะครับ โดยเก็บจากแหล่งข้อมูลในตารางนี้นะครับ แต่สารที่ตรงขอบเขตการศึกษาของเรา จะมีอยู่เพียง 2246 ชนิดเท่านั้น

## Slide 11
CAS | Name | A | B | C | Tmin | Tmax
50-00-0 | Methanal | 21.37 | 2204.13 | -30.15 | 190 | 271
51-66-1 | p-Methoxy-acetanilide | 20.27 | 3916.19 | -177.10 | 456 | 533
51-75-2 | N-Methylbis(2-chloroethyl)amine | 25.61 | 6563.29 | 0 | 273 | 333
541-35-5 | Butyramide | 22.08 | 4164.35 | -109.32 | 320 | 398
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Transform Data
Name | SMILES | A | B | C | Tmin | Tmax
Butyramide | CCCC(=O)N | 22.08 | 4164.35 | -109.32 | 320 | 398
Training
Test
Ref [4] PubChemPy documentation — PubChemPy 1.0.4 documentation, https://pubchempy.readthedocs.io/en/latest/guide/gettingstarted.html/
Use PubChem Database to
convert Name of compound to its SMILES
Methodology
Table 5. Psat Raw data
Notes: Since the database information, as shown above, does not include SMILES molecular formulas, we utilize the PubChem database to retrieve the SMILES data for each substance.
ถัดมานะครับ เนื่องจากข้อมูลที่ได้จากฐานข้อมูลเป็นดังตารางข้างบนนะครับ ซึ่งไม่มีสูตรโมเลกุล SMILES แสดงไว้ จึงต้องใช้ฐานข้อมูลที่มีชื่อว่า PubChem ทำการดึงข้อมูล SMILES ของสารแต่ละชนิดมา

## Slide 12
SMILES | VP1 | VP2 | VP3 | VP4 | VP5
CCCC(=O)N | 2.32 | 3.99 | 5.40 | 6.61 | 7.66
SMILES | A | B | C | Tmin | Tmax
CCCC(=O)N | 22.08 | 4164.35 | -109.32 | 320 | 398
Analysis & Cleansing
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Calculate the Vapor Pressure value using the Antoine equation, which is divided into 5 points according to Tmin and Tmax range, which can be shown in the table below.
Methodology
Note : VP – Vapor Pressure in ln(Psat), Psat in Pa, T in K
Notes: Next, we calculate the vapor pressure using the Antoine Equation at 5 points within the temperature range of Tmin to Tmax.

## Slide 13
Analysis & Cleansing
Outliers
Use boxplot to detect outliers
SMILES | VP1 | VP2 | VP3 | VP4 | VP5
CCCC(=O)N | 2.32 | 3.99 | 5.40 | 6.61 | 7.66
CC(CO)O | 9.89 | 10.36 | 10.79 | 11.19 | 11.57
. . | . . | . . | . . | . . | . .
COC1=CC=C(C=C1)CC=C | 4.85 | 7.15 | 8.93 | 10.35 | 11.52
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
After get the Vapor Pressure value of all substance, use Boxplot to see distribution of Vapor Pressure so that can we detect abnormal Vapor Pressure
Figure 5. Boxplot and Normal Distribution
Methodology
Table 6. SMILES and Vapor Pressure Data
2,246
datapoint
Notes: The vapor pressures for each substance are shown in table 6. Subsequently, we used a boxplot to visualize the distribution of the vapor pressure data and identify any outliers.

## Slide 14
Analysis & Cleansing
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Value | ln(Psat)
Min | -1.10 x 105
Max | 340.72
Point | 2,246
Value | ln(Psat) | Psat (atm)
Min | 2.09 | 8.1 x 10-5
Max | 15.78 | 71.58
Point | 1,787 | 
Methodology
Notes: From the plot on the left, there is a dataset with ln(Psat) values ranging from -100,000 to 340. After removing these outliers, we found that the vapor pressure values range from estimate 0 to 72 atm.

## Slide 15
Fingerprint Selecting
Training Data
80%
Test Data
20%
All Data |  | 
Alcohol | Alkyne | Carboxylic Acid
Aldehyde | Amide | Ester
Alkane | Amine | Ether
Alkene | Aromatic | Ketone
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
The best radius and bits for Fingerprint
Methodology
Fig 6. Heatmap Fingerprint for Psat modeling
Notes: To determine the appropriate number of bits and radius, we first divided the data into training and testing set, with a ratio of 80:20. We then further divided the data based on functional groups.
Next, we trained a simple model to find the optimal number of bits and radius. The heatmap analysis revealed that the model achieved the highest r2 with a radius of 4 and 4096 bits. We will use these values for the next model training.

## Slide 16
ML Algorithm | Hyperparameter
DT | max depth = None, min samples leaf = 1, min samples split = 2
RF | max depth = None, max feature = None, n estimators = 200
XGB | max depth = 5, learning rate = None, n estimators = 400
KNN | Algorithm = ball tree, n neighbors = 5, weights = distance
Training
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Note : Each ML algorithm use K-Fold with K = 5 and Grid Search
Methodology
Table 7. Setting of All Learning Algorithms
Notes: After identifying the best radius and bit, we proceeded to train models using various learning algorithms. For each algorithm, we found the best hyperparameter tuning, to improve model accuracy.
The optimal settings or hyperparameters for each algorithm are summarized in the following table 7

## Slide 17
Evaluation
Result
Method | MAE | MAPE (%) | RMSE | R2
DT | 0.80 | 15.00 | 1.38 | 0.68
KNN | 1.76 | 22.30 | 2.42 | -1.24
RF | 0.63 | 15.90 | 1.10 | 0.73
XGB | 0.59 | 13.60 | 1.06 | 0.80
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Table 8. Error metrics of each algorithm
Fig 7. Result of each algorithm
Notes: From the graph is showing the performance of the models in predicting Psat within the CHON range, it is evident that the best model is using the XGB algorithm. This model has the best MAE, MAPE, RMSE, and R2 values.

## Slide 18
Evaluation
Result
The functional group that this ln(Psat) prediction model can predict well is that the group that have condition with R2 ≥ 0.5 and MAPE ≤ 10%
Acceptable: Alcohol, Alkane, Alkyne, Alkene, Ketone
Unacceptable: Aromatic, Ester, Carboxylic Acid, Amide, Aldehyde, Amine, Ether
Fig 8. Psat Prediction on CHON Scope Group by Functional Group
Notes: With the results from the best model, we can further analyze which functional groups it can accurately predict. Functional groups with an R2 value greater than 0.5 and an MAPE less than 10% are considered well-predicted by this model.

## Slide 19
Calculation
Result
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Calculate A, B, C for Predicted ln(Psat) from the best model
Fig 9. Graph Distribution of Antoine Coefficients
Notes: When we use the results from the best model to calculate the Antoine coefficients, we observe that the values are distributed as shown in the graph.

## Slide 20
SMILES | Reference |  |  | Calculation |  |  | Train Temp Range (K)
 | A | B | C | A | B | C | 
2,4-Dimethyl-3-pentanol | 19.85 | 2370.74 | -127.05 | 20.35 | 2615.59 | -115.52 | 320 – 440
2-Butanamine, N-ethyl- | 21.24 | 3083.56 | -52.86 | 18.67 | 2006.16 | -96.46 | 283 – 313
Calculation
Result
Antoine Coefficients that yield similar results to the reference source, even if slightly different, can still be used reliably.
Table 8. Antoine Coefficients in this work and Antoine
Notes: Next, we plot the vapor pressure with Antione coefficients obtained with the temperature range from the reference data. This demonstrates that the vapor pressure values predicted by the model closely match those from the reference data.

## Slide 21
Calculation
Result
When comparing temperatures at different range, it is observed that greater temperature differences range lead to more accurate predictions compared to the reference, especially when considering the lowest and highest temperatures from all references for all substances.
SMILES | Reference |  |  | Calculation |  | 
 | A | B | C | A | B | C
2,4-Dimethyl-3-pentanol | 19.85 | 2370.74 | -127.05 | 20.35 | 2615.59 | -115.52
2-Butanamine, N-ethyl- | 21.24 | 3083.56 | -52.86 | 18.67 | 2006.16 | -96.46
320 – 437 K
283 – 313 K
Note: Temperature Range in Dataset (195 - 574 K)
Table 9. Antoine Coefficients in this work and Antoine
Notes: When we plot the graph outside the trained temperature range, we can see that there are still values close to the reference data. However, it is important to consider that the temperature range for the substance must be in the liquid phase.

## Slide 22
Conclusion
Use Morgan Fingerprint to resolve Previous Work Problem “Similar Structures, get same Features”
Use Morgan Fingerprint to establish Properties Prediction Model (Use for Organic Compound C, H, O and N) : Tb - CHON Scope with MAPE = 5.94% and R2 = 0.66 : ln(Psat) - CHON Scope with MAPE = 13.6% and R2 = 0.80
Learn about Machine Learning Algorithm, Cross Validation and Hyperparameter Tuning in each Algorithm and Neural Network Implementation for Improving Properties Prediction model

## Slide 23
Suggestions
Increasing the number of bits in a molecular fingerprint can help separate substructures, but some cases cannot be separated regardless of bit addition.
Deep Learning for modeling is more complex than Machine Learning, making it challenging to predict properties.
While modeling is faster, finding the right model takes time, so planning information preparation is crucial.
To improve model accuracy, consider creating a model that separates specific boundaries, focusing on specific functional groups.

## Slide 24
Q&A

## Slide 25
Backup

## Slide 26
Functional Group | Train | Test
Alcohol | 877 | 219
Aldehyde | 73 | 18
Alkane | 688 | 172
Alkene | 1628 | 407
Alkyne | 226 | 56
Amide | 394 | 99
Amine | 527 | 132
Aromatic | 930 | 233
Carboxylic Acid | 202 | 51
Ester | 3033 | 758
Ether | 10 | 3
Ketone | 354 | 88
Boiling Point
Backup

## Slide 27
Functional Group | Train | Test
Alcohol | 222 | 55
Aldehyde | 25 | 6
Alkane | 353 | 89
Alkene | 187 | 47
Alkyne | 31 | 8
Amide | 27 | 7
Amine | 65 | 16
Aromatic | 113 | 28
Carboxylic Acid | 42 | 11
Ester | 295 | 74
Ether | 6 | 1
Ketone | 63 | 16
Vapor Pressure Dataset
Backup

## Slide 28
SMILES | Referent |  |  | Calculation |  |  | Train Temp Range (K)
 | A | B | C | A | B | C | 
N,N-Diethyl-m-toluamide | 27.78 | 10187.29 | 80.94 | 17.01 | 3873.15 | 0.00 | 320 – 440
2-Methylglutaric anhydride | 22.34 | 5156.90 | -32.24 | 23.00 | 5920.64 | -39.84 | 283 – 313
Calculation
Backup
The reliability of Antoine Coefficients depends on the accuracy of the experimental data used in their calculation.

## Slide 29
Morgan Fingerprint
Step 1 : Specify indices in molecule
Step 2 : Specify substructure with given radius at each index
Backup
Ref [6] : Getting Started with the RDKit in Python, https://www.rdkit.org/docs/GettingStartedInPython.html#morgan-fingerprints-circular-fingerprints
Ref [7] : Extended-Connectivity Fingerprints ( Morgan Algorithm), https://doi.org/10.1021/ci100050t
r = 0
r = 1
r = 2

## Slide 30
Morgan Fingerprint
Ref [6] : Getting Started with the RDKit in Python, https://www.rdkit.org/docs/GettingStartedInPython.html#morgan-fingerprints-circular-fingerprints
Ref [7] : Extended-Connectivity Fingerprints ( Morgan Algorithm), https://doi.org/10.1021/ci100050t
Step 3 : Remove duplicate structure and store into Bit of fingerprint
Duplicate
Result
Bit 0 | Bit 1 | Bit 2 | Bit 3 | Bit 4 | … | Bit 539 | ... | Bit 791 | Bit 792 | … | Bit 1022 | Bit 1023
4 | 1 | 1 | 0 | 0 | … | 1 |  | 0 | 2 |  | 0 | 0
nBit = 1024
Backup

## Slide 31
SMILES
CCCC(=O)N (Butanamide)
Bit 0 | Bit 1 | Bit 2 | Bit 3 | Bit 4 | … | Bit 539 | ... | Bit 791 | Bit 792 | … | Bit 1022 | Bit 1023
4 | 1 | 1 | 0 | 0 | … | 1 | … | 0 | 2 | … | 0 | 0
Morgan Fingerprint
Backup
Converting the representation of molecule from text (SMILES) into number being called “Molecular Fingerprint”
r=2
1024 bits
Molecular Fingerprint
[4, 1, 1, 0, 0, …, 0, 0] (1024 number)

## Slide 32
Modeling for Psat Prediction
Backup
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Figure 2. Machine Learning workflow for Psat Prediction Modeling
Psat Prediction Model

## Slide 33
Method | MAE | MAPE(%) | RMSE | R2
DT | 0.482 | 725.9 | 2.790 | -6.551
KNN | 0.743 | 4887.0 | 3.287 | -14.23
RF | 0.439 | 161.4 | 2.883 | -22.37
XGB | 0.384 | 373.6 | 2.397 | -5.115
Evaluation
Backup
Analysis & Cleansing
Split Data
Data
Transform Data
Convert to Fingerprint
Model Training
Evaluation
Calculate ABC
Training
Test
Psat Prediction Evaluation
for Machine Learning

## Slide 34
Performance Evaluation
Where
N = amount of data
Mean Absolute Error
Mean Absolute Percentage Error
Coefficient of determination
Backup
Root Mean Square Error

## Slide 35
Ridge
Machine Learning Algorithms
Random Forest, RF
Backup

## Slide 36
XGBoost (Extreme Gradient Boosting), XGB
K-Nearest Neighbor, KNN
Machine Learning Algorithms
Backup

## Slide 37
Deep Learning (Neural Network), DL
Machine Learning Algorithms
Backup

## Slide 38
Graph Neural Network (GNN)
Backup
Ref [1] : Featurizers — deepchem 2.7.2.dev documentation, https://deepchem.readthedocs.io/en/latest/api_reference/featurizers.html
Ref [2] : DeepChem Github , https://github.com/deepchem/deepchem/blob/master/deepchem/feat/molecule_featurizers/mol_graph_conv_featurizer.py#L175
Ref [3] : GNN Project Explanation, https://www.youtube.com/watch?v=QLIkOtKS4os&list=PLV8yxwGOxvvoNkzPfCx2i8an--Tkt7O8Z&index=8

## Slide 39
PUFFIN Paper
Backup
Notes: https://pdf.sciencedirectassets.com/271348/1-s2.0-S0009250923X00190/1-s2.0-S000925092301179X/main.pdf?X-Amz-Security-Token=IQoJb3JpZ2luX2VjEBkaCXVzLWVhc3QtMSJIMEYCIQD6%2F1ic89%2B8gkn3yvjfucRq0ao%2FbedyWE8npxMlDS%2BkzgIhAL4gkcnu0JBO6oajJutDGER0CTrEjDkrulXhjExSrAjFKrMFCEEQBRoMMDU5MDAzNTQ2ODY1IgxAHgBAwv1OO%2F%2FDq%2B8qkAXWbP40tna9l6A4DwmXENugzDpgJdI3dOK%2F%2BO596CGaoTgOz8i9tAW%2FJV5zkvk76ermjW9LlnftwkwjIkHfwZBXFzbxhLAXaG8d7dCdh1VS467nSjGZkh7MFksUXN6wG7ensUuCQc%2FFGlduf%2BdC7u4drVhZaV2J3OxkJets4KoQwjb3YJQoZUF2vleOFWQ7iFAYkUXV2iV8qC1dlcIYNKFxa5M%2Baram3wvHfwHOVb57sxigKgRXWPZP2l4Ls2wN%2FHCbYWtxSRL8YAbD9r%2FmRnXvnw2U%2BOCiX9ZFZ6odXuef%2B%2BNfKNDnz4pRtU4VE24JvHtTh2lvmXJO0hhDpGwG0TL%2FCMwpVpT2pgmnXBx6ZJiypcwR3G2VQabVmV2XGREyrVFyuw%2FrWACYKPb0jdUEdFFAs0UmSjn%2Bf9Btv7kmWgXY7M2UCpW68Jrb4wAoXg64V23we%2FJwJ0lUnOYqq3YzGXS0%2FS%2F%2B7kK6H0pdknYuPEmVi3dM1NIh8DiDP5gStnbiDdD5av0HCSsK4VzuT859ICkzpyo%2BwbzHdZ8dHpoKe36mZ02sUSmDf5vIobCFedR%2FLNz505gqDvXiqbRXjXK1yl7Y79sr8VGQfb9udS1ZDDt9X0Xl0UZbF3%2FQzZsEFS2gy6AIMMQ9PhMN%2Bm9xxeMhwDigrIT6yT%2B6gWLdEPAnkeOLh1Qk6UopnvKvDcTi95iDi4Z3a9p%2Fmd6I7p0k5kIRa5vvleWkXND3elYQ%2FyAz9ROL4noPKDtoE5ucrvWDLpFXCBMfV91zi%2BnhAc%2BfvQwzsMz3KofvboMlBJ1RdkQv6tcHMmyuF602Oepr8naqqU5Fnkx2VStNRsWy6%2FWj4ugUSbqNKkbzIHczDO1R7oT3BPFVTjCP1qmwBjqwAWhczCd2Wf3zVgh42irALR7RARS4bfVORxHulJy8EZZ1%2FMLzCQeq0D4WYqGCRP3zFlBDa2Lx942MploCHRwAblaO5glqg%2BgM4W5p5kieyD%2FnWHQmWsUdMB0wLfxMA6A3EsL%2Fdoe1wzyydkM6XL%2BIMCP8pFgmiZzVAs3byxwpuwWsqyNwGtS8eqULtbQcBnaLlfp3JEHwgh%2BwrIcCj8ZzcPpAHavfYXpvBKrKwWr9Lyj7&X-Amz-Algorithm=AWS4-HMAC-SHA256&X-Amz-Date=20240401T085840Z&X-Amz-SignedHeaders=host&X-Amz-Expires=300&X-Amz-Credential=ASIAQ3PHCVTY5IGE7K6O%2F20240401%2Fus-east-1%2Fs3%2Faws4_request&X-Amz-Signature=93de3cfb5904219e5d3abd9d592e152b383e4040647e6a49f11a3b960053e0ff&hash=54c49de18cd2b6e54622881c460253d4208caeead00824131b0fb398955c0a33&host=68042c943591013ac2b2430a89b270f6af2c76d8dfd086a07176afe7c76c2c61&pii=S000925092301179X&tid=spdf-417ceb13-9c56-4253-9669-324addc1254e&sid=5640448f6745d447bd18ac3095e1f2243240gxrqb&type=client&tsoh=d3d3LnNjaWVuY2VkaXJlY3QuY29t&ua=110f5a5802515156075f&rr=86d760f02e838342&cc=th

## Slide 40
PUFFIN Paper
Backup
Notes: https://pdf.sciencedirectassets.com/271348/1-s2.0-S0009250923X00190/1-s2.0-S000925092301179X/main.pdf?X-Amz-Security-Token=IQoJb3JpZ2luX2VjEBkaCXVzLWVhc3QtMSJIMEYCIQD6%2F1ic89%2B8gkn3yvjfucRq0ao%2FbedyWE8npxMlDS%2BkzgIhAL4gkcnu0JBO6oajJutDGER0CTrEjDkrulXhjExSrAjFKrMFCEEQBRoMMDU5MDAzNTQ2ODY1IgxAHgBAwv1OO%2F%2FDq%2B8qkAXWbP40tna9l6A4DwmXENugzDpgJdI3dOK%2F%2BO596CGaoTgOz8i9tAW%2FJV5zkvk76ermjW9LlnftwkwjIkHfwZBXFzbxhLAXaG8d7dCdh1VS467nSjGZkh7MFksUXN6wG7ensUuCQc%2FFGlduf%2BdC7u4drVhZaV2J3OxkJets4KoQwjb3YJQoZUF2vleOFWQ7iFAYkUXV2iV8qC1dlcIYNKFxa5M%2Baram3wvHfwHOVb57sxigKgRXWPZP2l4Ls2wN%2FHCbYWtxSRL8YAbD9r%2FmRnXvnw2U%2BOCiX9ZFZ6odXuef%2B%2BNfKNDnz4pRtU4VE24JvHtTh2lvmXJO0hhDpGwG0TL%2FCMwpVpT2pgmnXBx6ZJiypcwR3G2VQabVmV2XGREyrVFyuw%2FrWACYKPb0jdUEdFFAs0UmSjn%2Bf9Btv7kmWgXY7M2UCpW68Jrb4wAoXg64V23we%2FJwJ0lUnOYqq3YzGXS0%2FS%2F%2B7kK6H0pdknYuPEmVi3dM1NIh8DiDP5gStnbiDdD5av0HCSsK4VzuT859ICkzpyo%2BwbzHdZ8dHpoKe36mZ02sUSmDf5vIobCFedR%2FLNz505gqDvXiqbRXjXK1yl7Y79sr8VGQfb9udS1ZDDt9X0Xl0UZbF3%2FQzZsEFS2gy6AIMMQ9PhMN%2Bm9xxeMhwDigrIT6yT%2B6gWLdEPAnkeOLh1Qk6UopnvKvDcTi95iDi4Z3a9p%2Fmd6I7p0k5kIRa5vvleWkXND3elYQ%2FyAz9ROL4noPKDtoE5ucrvWDLpFXCBMfV91zi%2BnhAc%2BfvQwzsMz3KofvboMlBJ1RdkQv6tcHMmyuF602Oepr8naqqU5Fnkx2VStNRsWy6%2FWj4ugUSbqNKkbzIHczDO1R7oT3BPFVTjCP1qmwBjqwAWhczCd2Wf3zVgh42irALR7RARS4bfVORxHulJy8EZZ1%2FMLzCQeq0D4WYqGCRP3zFlBDa2Lx942MploCHRwAblaO5glqg%2BgM4W5p5kieyD%2FnWHQmWsUdMB0wLfxMA6A3EsL%2Fdoe1wzyydkM6XL%2BIMCP8pFgmiZzVAs3byxwpuwWsqyNwGtS8eqULtbQcBnaLlfp3JEHwgh%2BwrIcCj8ZzcPpAHavfYXpvBKrKwWr9Lyj7&X-Amz-Algorithm=AWS4-HMAC-SHA256&X-Amz-Date=20240401T085840Z&X-Amz-SignedHeaders=host&X-Amz-Expires=300&X-Amz-Credential=ASIAQ3PHCVTY5IGE7K6O%2F20240401%2Fus-east-1%2Fs3%2Faws4_request&X-Amz-Signature=93de3cfb5904219e5d3abd9d592e152b383e4040647e6a49f11a3b960053e0ff&hash=54c49de18cd2b6e54622881c460253d4208caeead00824131b0fb398955c0a33&host=68042c943591013ac2b2430a89b270f6af2c76d8dfd086a07176afe7c76c2c61&pii=S000925092301179X&tid=spdf-417ceb13-9c56-4253-9669-324addc1254e&sid=5640448f6745d447bd18ac3095e1f2243240gxrqb&type=client&tsoh=d3d3LnNjaWVuY2VkaXJlY3QuY29t&ua=110f5a5802515156075f&rr=86d760f02e838342&cc=th